## Slide 1: Procyon: Promoting Fine-Grain Multi-Tenancy to Optimize Sparse Streaming Accelerators
Ubaid Bakhtiar, Jeremy Sha, Helya Hosseini, Bahar Asgari
Corresponding author: ubaidb@umd.edu
University of Maryland, College Park

## Slide 2: Existence of Sparsity
Scientific Computing
Large Language Models
Recommendation Systems
Computer Vision
Speech Processing
1

## Slide 3: Streaming Accelerators
Data-driven execution model of streaming accelerators
Maximize the data transfer as well as computational throughput
Schedule the data for a compute engine in the corresponding memory channel
HBM Channel 0
HBM Channel 1
HBM Channel 2
HBM Channel 4
Compute Engine 0
Compute Engine 1
Compute Engine 2
Compute Engine 3
HBM Channel 5
HBM Channel 6
HBM Channel 7
HBM Channel 8
Input
Output
2

## Slide 4: CHALLENGES

## Slide 5: Poor Data Scheduling
1. PE-aware Non-zero Scheduling
r0_op1 = 1A
r4_op1 = 11A
r8_op1 = 21B
r12_op1 = 31A
r16_op1 = 41D
r36_op1 = 51B
I1:
I2:
I3:
I4:
I5:
I6:
PE0 of Channel 0 Instructions:
0.60
Throughput:
PE0 underutilization:
= 40%
RAW
r0_op2 = 2B +r0_op1
I7:
Pipeline of PE-aware Non-zero Scheduling
3
L. Song et.al Serpens DAC 2022

## Slide 6: Poor Data Scheduling
2. Cross-HBM Channel OoO Scheduling
r80_op1_sh =61A
r81_op1_sh =71C
r82_op1_sh =81B
i8:
i9:
i10:
PE0 of Channel 1 instructions:
Pipeline of PE-aware Non-zero Scheduling
0
CrHCS schedule these instructions to the PEs of Channel 0
4
U. Bakhtiar et.al Chason MICRO 2025

## Slide 7: Poor Data Scheduling
r80_op1_sh =61A
r81_op1_sh =71C
r82_op1_sh =81B
i8:
i9:
i10:
PE0 of Channel 1 instructions:
CrHCS schedule these instructions to the PEs of Channel 0
1 non-zero per cycle
Throughput:
PE0 underutilization: = 10%
Pipeline of CrHCS
2. Cross-HBM Channel OoO Scheduling
0
5
U. Bakhtiar et.al Chason MICRO 2025
Notes: - animation ?

## Slide 8: Poor Data Scheduling
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
PE-aware | 16.83 | 20.44 | 20.94 | 26.84 | 27.66 | 28.42 | 28.78 | 34.91 | 35.03 | 35.2 | 37.81 | 47 | 48.17 | 49.29 | 51.4 | 52.92 | 54.53 | 54.85 | 56.95 | 59.66 | 60.47 | 64.57 | 64.8 | 66.67 | 67.11 | 68.29 | 73.13 | 73.3 | 84.04 | 84.15 | 85.67 | 88.37 | 90.8 | 91.3 | 91.58 | 94
CrHCS | 4.86 | 8.09 | 8.12 | 9.23 | 12.6 | 13.4 | 17.04 | 17.62 | 17.7 | 18.66 | 19.29 | 19.33 | 20.28 | 23.72 | 25.21 | 25.74 | 26.15 | 26.84 | 27.9 | 28.42 | 28.96 | 30.77 | 32.49 | 32.81 | 33.07 | 33.46 | 37.22 | 39.41 | 43.38 | 46.7 | 46.96 | 50.26 | 50.51 | 52.45 | 64.83 | 83.96
36 SuiteSparse Workloads
PE Underutilization (%)
Both PE-aware and CrHCS results in considerable number of stalls
This results in high PE underutilization, resulting in sub-optimal performance
6

## Slide 9: Single Workload Execution Model
SOTA sparse streaming accelerators follows a single workload execution model
Multiple workloads on a single accelerator must be executed sequentially
Deploying multiple accelerators for concurrent execution increase the system cost
Sparse Accelerator
Input
Output
Underutilization
Single-Tenant
Underutilization
Sparse Accelerator
Input
Output
7

## Slide 10: OUR WORK

## Slide 11: Main Goal
Sparse Accelerator
Input
Output
Underutilization
Multi-Tenancy
Allow multiple workloads to execute on a single sparse streaming accelerator
Improve the PE underutilization inherit in current data scheduling techniques
The main goal of Procyon is to:
8

## Slide 12: Key Insight
“If we fuse the PE instructions of multiple workloads into a unified set of instructions, it enables multi-tenant execution of a PE while eliminating PE stalls by filling them with instructions from other workloads.”
9

## Slide 13: Procyon Scheduler – Level of Granularity
Accelerator switches between multiple workloads alternatively
Compute and write stages are sequential
A single accelerator is used
Coarse Grain Multi-Tenancy
Unified compute for multiple workloads
Parallel write operations
A single accelerator is used but with higher PE utilization
Fine Grain Multi-Tenancy
10

## Slide 14: Procyon Scheduler – Level of Granularity
Accelerator switches between multiple workloads alternatively
Compute and write stages are sequential
A single accelerator is used
Coarse Grain Multi-Tenancy
Unified compute for multiple workloads
Parallel write operations
A single accelerator is used but with higher PE utilization
Fine Grain Multi-Tenancy
11

## Slide 15: Procyon Scheduler – Mechanism
Key Idea: To fuse the instructions of a PE from one workload with those of a PE from another workload, making it a multi-tenant PE.
12

## Slide 16: Procyon Architectural Support
13

## Slide 17: Procyon Architectural Support
14
A general sparse streaming accelerator
A Procyon-compatible general sparse streaming accelerator

## Slide 18: KEY RESULTS

## Slide 19: PE Underutilization
Procyon compatible baselines achieves lower PE underutilization under all PE pairing schemes as multiple workloads are being executed on each PE.
PE underutilization % of Serpens and Chason with and without Procyon on SuiteSparse Workloads (lower is better)
15

## Slide 20: Speedup
The lower PE underutilization as well as multi-tenancy results in speedup over sequential execution of the workloads on baselines
Latency speedup of Procyon vs. Serpens and Chason on SuiteSparse workloads groups (higher is better)
16

## Slide 21: Throughput
Procyon compatible baselines achieves higher throughput due to increased activity of PEs
Throughout of Serpens and Chason with and without Procyon on SuiteSparse Workloads (higher is better)

## Slide 22: Conclusions
Sparsity is a prevalent topic in scientific computing as well as generative AI
Sparse streaming accelerators have shown strong performance gains
Procyon compatible streaming accelerators achieves substantial improvement in PE underutilization, performance and system’s monetary cost
Existing sparse streaming accelerators are highly underutilized as well as follow a single workload execution model  sub-optimal performance and increased system cost
We propose Procyon to fuse the instructions of multiple workloads and execute them on a single sparse streaming accelerator concurrently
To support Procyon, we showed the architectural extension for a streaming accelerator
17
FPGA

## Slide 23
Speaker:
Ubaid Bakhtiar
5th Year ECE Ph.D. Candidate
ubaidb@umd.edu
THANK YOU !!!
Computer Architecture & Systems Lab